## Slide 1: Wrap-up and Next Steps
Linda M. Katz, M.D., M.P.H.
Director, FDA’s Office of Cosmetics and Colors
Center for Food Safety and Applied Nutrition
February 4, 2020

## Slide 2: Points of Discussion
Mineral fibers of potential concern in talc
Mineral fibers in the lung: exposure and toxicity
Preliminary recommendations from the IWGACP
  Mineral fiber terminology and definitions
  Analytical approach
  Content and format of analytical reports, research needs
Public Comments

## Slide 3: Mineral Fibers of Potential Concern in Talc
Because specific geological conditions that form talc can result in some internal variation (variability in mineral composition) within the mine, talc ores used for cosmetic raw material talc would benefit from a comprehensive mineralogic assessment.

## Slide 4: Mineral Fibers in the Lung: Exposure and Toxicities
Asbestos and EMPs can cause cancers and non-cancer health effects.
Proposed mechanism of action is via inflammatory response.
EMP characteristics potentially influencing this process include:
  Length and width,
  Mineral type,
  Persistence in biological tissue,
  Surface area,
  Surface reactivity, and
  Surface charge (Zeta potential).

## Slide 5: Preliminary Recommendations from the IWGACP
Adoption of the term EMP as “any mineral particle with a minimum aspect ratio of 3:1”.
Testing laboratories should report all EMPs having length ≥ 0.5 µm.
Test methods should specify reportable EMPs identified as amphibole or chrysotile particles as covered minerals.
Test methods should include directions enabling reporting and counting of primary and secondary structures (e.g., bundles, clusters and fibers) of covered EMPs as a function of sample mass.

## Slide 6: Preliminary Recommendations from the IWGACP
PLM is a required analysis of each sample using established guideline methods. XRD is also a useful method for detecting asbestos; however, it may be limited due to sensitivity.
Use of TEM with EDS and SAED to address deficiencies in sensitivity that cause false negatives by PLM.
  Scanning electron microscopy might be useful as a complementary method, but currently has significant shortcomings for identification of chrysotile.
“Mass percent,” a unit that is frequently used to express content of asbestos in commercial bulk materials, is not appropriate for measurement of EMPs in talc and products containing talc.
  Mass percent does not correlate with the number of fibers.
  A single, atypically-wide EMP could dominate and skew the calculation of mass percent.

## Slide 7: Additional Needs
  Research to minimize false negative/positive rates; improve sensitivity and accuracy of counting.
    Determine sources of variation in sampling.
    Improve sample preparation methods (e.g., “concentration methods”).
    Reference standards specific to talc and talc-containing products.
  Validation of analytical methods (XRD, PLM, TEM) specific to talc and cosmetic products containing talc.
    Increase laboratory and analyst proficiency.
    Increase inter-laboratory concurrence.

## Slide 8: Next Steps
The IWGACP will continue its work on these and other topics specifically related to health.
Review information obtained in this meeting and submitted to the docket FDA-2020-N-0025 which closes on March 4, 2020.
Complete and post a White Paper addressing issues presented in the Executive Summary, as well as from this and other recent meetings, and the docket.

## Slide 9: Special Thanks to the Following:
From CFSAN
  Debbie Smegal
  Steve Wolfgang
  Susan Spence
  Denise Hodge
  Caroline Linder
  Janesia Robbs
  Kari Barrett
  Juanita Yates
  Lindsay Haake
  Jessica Larkin
  Phil Chao
  Doug Ticker
Work Group Members and others:
  Paul Howard
  Brad Van Gosen
  Chris Weis
  Dayle Cristinzio
  Beth Fritsch
  Steve Morin
  Monique Richards
  Alyssa Polovoy
  And our other federal partners and work group members